## Slide 1: Software Implementation of ECC2-131
刘志杰

## Slide 2: Catalog
ECC2-131 Finite Field Construction
ECC2-131 Addition
ECC2-131 Reduction
ECC2-131 Square
ECC2-131 Multiplication
ECC2-131 Inversion
ECC2-131 Square Root
ECC2-131 Solving the Quadratic Equation

## Slide 3: ECC2-131 Finite Field Construction
, ()

## Slide 4
We assume that the implementation platform has a W-bit architecture where W is a multiple of 64. The bits of a W-bit word U are numbered from 0 to W −1, with the rightmost bit of U designated as bit 0.
The following standard notation is used to denote operations on words U and V :
U ⊕V bitwise exclusive-or
U &V bitwise AND
U >> i right shift of U by i positions with the i high-order bits set to 0
U << i left shift of U by i positions with the i low-order bits set to 0.
Let f (x) be an irreducible binary polynomial of degree m, and write The elements of are the binary polynomials of degree at most m −1.
Addition of field elements is the usual addition of binary polynomials. Multiplication is performed modulo f (x). A field element is associated with the binary vector of length m.
In software, a may be stored in an array of t W-bit words: A = (A[t −1], . . ., A[2], A[1], A[0]), where the rightmost bit of A[0] is a0, and the leftmost s bits of A[t −1] are unused (always set to 0).

## Slide 5: ECC2-131 Addition
⊕ bitwise exclusive-or
算法实现：
Notes: R9 是 第四个 b0; rdx 是 a0
Rcx 是第一个 a1 r8 是b1
加入inline

## Slide 6: Common
Notes: 0.328 ns

## Slide 7: ECC2-131 Reduction
Recall that ,where r (x) is a binary polynomial of degree at most m −1. Algorithm 2.40 reduces c(x) modulo f (x) one bit at a time, starting with the leftmost bit. It is based on the observation that
The reduction is accelerated by precomputing the polynomials , 0 ≤ k ≤ W −1.
If r (x) is a low-degree polynomial, or if f (x) is a trinomial, then the space requirements
are smaller, and furthermore the additions involving in step 2.1 are faster. The
following notation is used: if C = (C[n], . . .,C[2],C[1],C[0]) is an array, then C{ j }
denotes the truncated array (C[n], . . .,C[ j +1],C[ j ]).

## Slide 8: Fast reduction modulo
If f (x) is a trinomial, or a pentanomial with middle terms close to each other, then reduction of c(x) modulo f (x) can be efficiently performed one word at a time. For example, m = 131 and W = 64 and consider reducing the word C[4] of c(x) modulo . The word C[4] represents the polynomial . We have
By considering the four columns on the right side of the above congruences, we see that reduction of C[4] can be performed by adding C[4] four times to C, with the rightmost bit of C[4] added to bits 138, 127, 126 and 125 of C;

## Slide 9
C[2]
C[1]
10
C[4]
⊕
C[4]
C[4]
1
⊕
⊕
C[4]
⊕
2
3

## Slide 10
Algorithm： Fast reduction modulo (with W = 64)
INPUT: A binary polynomial c(x) of degree at most 260.
OUTPUT: c(x) mod f (x).
1. For i from 4 downto 3 do {Reduce C[i ] modulo f (x)}
1.1 T←C[i ].
1.2 C[i −3]←C[i −3] ⊕ () ⊕ () ⊕ ().
1.3 C[i −2]←C[i −2] ⊕ () ⊕ () ⊕ () ⊕ ().
1.4 C[i −1]←C[i −1] ⊕ () .
2. T←C[2] . {Extract bits 3–63 of C[2]}
3. C[0]←C[0] ⊕ () ⊕ () ⊕ () ⊕ ().
4. C[1]←C[1] ⊕ () .
5. C[2]←C[2]&0x7. {Clear the reduced bits of C[2]}
6. Return (C[2],C[1],C[0]).

## Slide 12: ECC2-131 Square
Since squaring a binary polynomial is a linear operation, it is much faster than multiplying
two arbitrary polynomials; i.e., if
then
The binary representation of is obtained by inserting a 0 bit between consecutive
bits of the binary representation of as shown in below. To facilitate this process,
a table T of size 512 bytes can be precomputed for converting 8-bit polynomials
into their expanded 16-bit counterparts. Algorithm 2.39 describes this procedure for
the parameter W = 32.

## Slide 13: ECC2-131 Multiplication

## Slide 17: ECC2-131 Inversion
Notes: 17 10
17=10 +7 7=17-7 1=7-2*3
10 = 7+ 3 3=10-7 =7-2*(10-7)
7=2*3 +1 1=7-2*3 =(-2)*10 +3*7
=(-2)*10+3*(17-10)
=(-5)*10+3*17

## Slide 21
Make sure that deg(u) ≥ deg(v) and j = deg(u)−deg(v), then one computes
. By Theorem 2.46, gcd(u,v) = gcd(r,v).
Notes: 一次不一定是 deg(u)<deg(v).多次之后，就会是
实质就是 r = a – z*b;

## Slide 22
Notes: 然后，a 和 b 以及余数要写出 ad + bc的形式

## Slide 23
Notes: Ag+fh=1 mod f >>> ag mod f + fh mod f = 1mod f >>> ag mod f ==1 因为 fh mod f =0

## Slide 28
Algorithm Almost Inverse Algorithm for inversion in
INPUT: A nonzero binary polynomial a of degree at most m −1.
OUTPUT: mod f .
1. , .
2. , .
3. While () do
3.1 While z divides u do
.
3.2 If deg(u) < deg(v) then .
3.3
4. .
5. Return().